Με άξονα την άσκηση με 3 δρομολογητές (RIP routing) έχουμε την εξής παραλλαγή :

Για τον Πρώτο Δρομολογητή :

hostname Central

enable secret test

interface FastEthernet0/0

description LAN of router Central

ip address 192.168.10.1 255.255.255.0

interface Serial0/0

description Link to THIRD

bandwidth 2048

ip address 192.168.22.1 255.255.255.0

clock rate 64000

interface Serial0/1

description Link to SECOND

ip address 192.168.21.1 255.255.255.0

clock rate 64000

bandwidth 128

router ospf 1

network 192.168.10.0 0.0.0.255 area 0

network 192.168.21.0 0.0.0.255 area 0

network 192.168.22.0 0.0.0.255 area 0

Για τον Δεύτερο Δρομολογητή :

hostname SECOND

enable secret test

interface FastEthernet0/0

description LAN of router SECOND

ip address 192.168.20.1 255.255.255.0

interface Serial0/0

description Link to Central

ip address 192.168.21.2 255.255.255.0

bandwidth 128

interface Serial0/1

bandwidth 2048

ip address 192.168.23.2 255.255.255.0

clock rate 64000

router ospf 1

network 192.168.20.0 0.0.0.255 area 0

network 192.168.21.0 0.0.0.255 area 0

network 192.168.23.0 0.0.0.255 area 0

Για τον Τρίτο Δρομολογητή :

hostname THIRD

enable secret test

interface FastEthernet0/0

description LAN of router THIRD

ip address 192.168.30.1 255.255.255.0

interface Serial0/0

description Link to Central

bandwidth 2048

ip address 192.168.22.2 255.255.255.0

interface Serial0/1

bandwidth 2048

ip address 192.168.23.1 255.255.255.0

router ospf 1

network 192.168.22.0 0.0.0.255 area 0

network 192.168.23.0 0.0.0.255 area 0

network 192.168.30.0 0.0.0.255 area 0

Τώρα προσπαθήστε να ‘τρέξετε’ την εντολή tracert από το Η/Υ με IP: 192.168.20.11 στον απέναντι Η/Υ με IP την : 192.168.10.11 και παρατηρήστε την διαδρομή που ακολουθεί. Μετά αλλάξτε στους router με την ρύθμιση του interface τους με bandwidth των 128k, σε 4096.

Δώστε τις παρακάτω εντολές σε καθένα από τους τρείς routers :

show ip route

show ip ospf interface

(show ip ospf network

show ip ospf database)